## Slide 1: Overview Autonomous Vehicles
Joseph E. Gonzalez
jegonzal@cs.berkeley.edu

## Slide 2: What is the problem?
Driving is hard and wasteful.
Transportation is expensive.

## Slide 4: Human Drivers are the Problem
In the United States (2016)
7,277,000 reported crashes
3,144,000 people were injured
37,461 fatalities (1 fatality every 14 minutes)
  Leading cause of death for ages 16-22
94% of all crashes are due to human error
https://crashstats.nhtsa.dot.gov/Api/Public/ViewPublication/812580
We should be working on this problem!

## Slide 5: Why now? Why us?
Sensing and actuation are (mostly) solved problems
  Unlike many robotics tasks
Limited by perception (alg.) and compute (arch./sys.)
  Current research focus is on AI
    Needed for advanced autonomy
    AI needed for collision avoidance is partly ready
  Gap in research on systems side
    Needed: software and hardware platform of an autonomous vehicles
    Keep device costs down while enabling innovation
Challenges to entry
  Data and test platform  simulation is improving + Berkeley test vehicles

## Slide 6: Basics of Autonomous Vehicles

## Slide 7: Levels of Autonomy: Automotive Engineering Society (AES) Standard
 | Name | Description | Steering & Accel. | Env. Monitor | Fallback
1 | Driver Assistance | Assistance for either steering or acceleration using information about env. with the expectation that human performs all remaining aspects. | Human + System | Human | Human
2 | Partial Automation | Assistance for both steering and acceleration using information about env. with the expectation that human performs all remaining aspects. | System | Human | Human
3 | Conditional Automation | Autonomous driving with the expectation that human will respond to a request to intervene | System | System | Human
4 | High Automation | Autonomous driving with the ability to take a safe action (e.g., pull over) if a human cannot intervene. | System | System | System
5 | Full Automation | Autonomous driving under all feasible roadway and environmental conditions. | System | System | System

## Slide 8: Advanced Driver Assistance Systems (ADAS) vs Autonomous Vehicles
Level 4 – Level 5 Autonomy
Levels of Full Autonomy
Level 4
Full autonomy in constrained situations
Level 5
Fully autonomous in all situations
Level 1– Level 3 ADAS Systems
L1: Individual assistance functions
Collision warning
Pedestrian detection
Automatic emergency braking
Lane detection, lane assist
Parking assist
L2: combining them
L3: vehicle takes over driving functions, but driver must be ready to take over

## Slide 9: Cartoon Autonomous Vehicles Pipeline
Current
State
Cameras
LiDAR
Radar
Object Det.
Lane Detection
IMU
GPS
Localization
Pose Est.
Sensing
Perception
Planning
Path Planning
Steering
Control
Accel & Breaking
Specialized
Scenarios
Future
States
Prediction
Prediction

## Slide 10: Tesla Sensor Package

## Slide 11: Sensors – Top View
Camera array
360° LiDAR
Stereo camera pairs
LiDAR
& Radar

## Slide 12
Waymo

## Slide 13: Sensors and Their Uses

## Slide 14: Sensor Comparison
Sensor | Relative Cost | Resolution | Strengths | Weaknesses
LiDAR | Highest | Mid-range | Depth data 360° view | Susceptible to weather (fog, rain, snow etc.)
Camera | Least expensive | Highest | Traffic lights, pedestrians, signage | Darkness, glare, fog,
RADAR | Cheap | Low | Robust in bad weather | Low Resolution
SONAR | Cheap | Very low | Robust in weather, darkness, brightness | Very Short Range

## Slide 15: Applying DNN to Integrated Sensor Data
Integrating
Multiple
Sensors
Point cloud
RGB-D image
Object Detection
Occupancy Grid
LIDAR
CAMERAS
RADAR
ULTRASONIC
(short-range)
Lane Segmentation
Object Tracking
Notes: Learning-Defined Sensor Fusion
  We're using DL rather than straight SW
Sensor Virtualization

## Slide 16: Typical Approach to State Representation
Current
State
Accurate 3D Models
Individual object detection localization, and pose estimation
High-resolution maps
Object trajectories
8.2m
6.5m
12.1m
4.3m
10.6 m
11.3 m

## Slide 17
Waymo

## Slide 18: Cartoon Autonomous Vehicles Pipeline
Current
State
Cameras
LiDAR
Radar
Object Det.
Lane Detection
IMU
GPS
Localization
Pose Est.
Sensing
Perception
Planning
Path Planning
Steering
Control
Accel & Breaking
Specialized
Scenarios
Future
States
Prediction
Prediction

## Slide 19: Classic Hierarchical Approach
Decompose motion planning and control into stages
Route Planning
Merge Left
Yield to
Ped.
Park
Follow
Lane
Exit
Ramp
Merge
Right
Overtake
Behavior Planning
Path Planning
Local Control
Sequence of roads and intersections
Target State Configurations
Detailed Path to Follow
Road Networks Traffic Information
Obstacles …
Model of the world around the car including predicted future states.
Model of the vehicle’s dynamics.
Notes: Path planning image courtesy of http://www.smart2zero.com/news/elektrobit-rolls-four-more-software-modules-autonomous-driving
Control image courtesy of https://www.egypt-business.com/Ticker/details/1738-Worldwide-Electronic-Stability-Control-ESC-Market-Growth-Projection-to-2021/159246

## Slide 20
Current
State
Cameras
LiDAR
Radar
Object Det.
Lane Detection
IMU
GPS
Localization
Pose Est.
Sensing
Perception
Planning
Path Planning
Steering
Control
Accel & Breaking
Specialized
Scenarios
Future
States
Prediction
Prediction
The Architectural Implications of Autonomous Driving
  Presented by Sukrit
ChauffeurNet: Learning to Drive by Imitating the Best and Synthesizing the Worst
  Presented by Dequan
Previous
Computer Vision Reading

## Slide 21: Readings today
The Architectural Implications of Autonomous Driving
  Presented by Sukrit
ChauffeurNet: Learning to Drive by Imitating the Best and Synthesizing the Worst
  Presented by Dequan
Discussion about research opportunities and challenges

## Slide 22: Route Planning
Determine best route between origin and destination
  survey “Route Planning in Transportation Networks”
Input: source and destination as well as the road network, traffic information, obstacles
Output: Sequence of roads (paths) including GPS coordinates.
Relies on optimizations of classic graph algorithms to plan in seconds across entire contents.
Route Planning
Sequence of roads and intersections
Road Networks Traffic Information
Obstacles …
Google Maps
Apple Maps
Big Maps

## Slide 23: Classic Hierarchical Approach
Decompose motion planning and control into stages
Route Planning
Path Planning
Local Control
Detailed Path to Follow
Road Networks Traffic Information
Obstacles …
Model of the world around the car including predicted future states.
Model of the vehicle’s dynamics.
Merge Left
Yield to
Ped.
Park
Follow
Lane
Exit
Ramp
Merge
Right
Overtake
Behavior Planning
Sequence of roads and intersections
Target State Configurations
Notes: Path planning image courtesy of http://www.smart2zero.com/news/elektrobit-rolls-four-more-software-modules-autonomous-driving
Control image courtesy of https://www.egypt-business.com/Ticker/details/1738-Worldwide-Electronic-Stability-Control-ESC-Market-Growth-Projection-to-2021/159246

## Slide 24: Behavior Planning
Determines the high-level actions need to move through the input road network in response to observations and future state predictions.
  Example:
    Exit right from parking lot.
    Merge into left lane
    Turn left at intersection
    Avoid [observed] construction worker ...
Inputs: Road sequence as well as observations and predictions from perception systems.
Outputs: Actions which can be mapped to state configurations (e.g., GPS waypoints, orientation, speed…)
Solutions: Finite state machines as well as probabilistic generalizations (MDPs).
  Area of potential future innovation  Learned behaviors
Merge Left
Yield to
Ped.
Park
Follow
Lane
Exit
Ramp
Merge
Right
Overtake
Behavior Planning
Sequence of roads and intersections
Target State Configurations

## Slide 25: Classic Hierarchical Approach
Merge Left
Yield to
Ped.
Park
Follow
Lane
Exit
Ramp
Merge
Right
Overtake
Behavior Planning
Sequence of roads and intersections
Decompose motion planning and control into stages
Route Planning
Local Control
Road Networks Traffic Information
Obstacles …
Model of the world around the car including predicted future states.
Model of the vehicle’s dynamics.
Target State Configurations
Path Planning
Detailed Path to Follow
Notes: Path planning image courtesy of http://www.smart2zero.com/news/elektrobit-rolls-four-more-software-modules-autonomous-driving
Control image courtesy of https://www.egypt-business.com/Ticker/details/1738-Worldwide-Electronic-Stability-Control-ESC-Market-Growth-Projection-to-2021/159246

## Slide 26: Path Planning
Compute an “optimal” sequence of state configurations (e.g., locations and velocities) that terminates in the desired end state.
Path: sequence of state configurations including
  Position, orientation, velocity
Optimal
  Feasible with respect to vehicle dynamics
  Avoid collisions or violating road laws
  Comfortable (limited acceleration, jerk, …)
  Efficient (reduce wasted energy and time)
Dependencies
  Road network
  Behavior of other vehicles and pedestrians
  Vehicle dynamics model
Hard problem but well studied!
Target State Configurations
Path Planning
Detailed Path to Follow

## Slide 27: Vehicle Dynamics Models
Typically adopt simplified physical model of vehicle dynamics that capture constraints on the velocity and acceleration of the vehicle to determine feasible paths.
Feasible
Infeasible
Infeasible
Common Dynamics Models
Single Track No Slip
Single Track with Frictional Forces
Used in low speed settings
(e.g., Parking)
Needed for driving at higher speeds.
(e.g., highway driving)
Illustrations of dynamics models from “A Survey of Motion Planning and Control Techniques for Self-driving Urban Vehicles”
Notes: Note that vehicle stability control systems often use even more elaborate models that capture the frame and tire stiffness and cornering characteristics of the vehicle.

## Slide 28: Optimal Path Planning Problem
Path Objective Function
Comfort + Safety
path
Set of all continuous paths
Optimization Problem:
Path terminates in a goal state (e.g., car is parked)
Constraints:
The path remains in the drivable space
(obeys laws and doesn’t hit obstacles)
Differential Constraints on path curvature (given by vehicle dynamics)
Solving the general problem is PSPACE-hard

Notes: Pspace-Hard means it is at least as hard as an NP-complete problems.

## Slide 29: Approximate Solutions to Optimal Path Planning
Variational Methods
Graph Search Methods (commonly used)
Approximate smooth paths with parametric functions (e.g., splines) and optimize control points.
Get stuck in local minima
Discretize space of possible paths and optimize
Regular Lane or Geometric Graphs
Random or Incremental Graphs

## Slide 30: Classic Hierarchical Approach
Decompose motion planning and control into stages
Route Planning
Merge Left
Yield to
Ped.
Park
Follow
Lane
Exit
Ramp
Merge
Right
Overtake
Behavior Planning
Local Control
Sequence of roads and intersections
Road Networks Traffic Information
Obstacles …
Model of the world around the car including predicted future states.
Model of the vehicle’s dynamics.
Steering Angle
Acceleration
Path Planning
Target State Configurations
Detailed Path to Follow
Notes: Path planning image courtesy of http://www.smart2zero.com/news/elektrobit-rolls-four-more-software-modules-autonomous-driving
Control image courtesy of https://www.egypt-business.com/Ticker/details/1738-Worldwide-Electronic-Stability-Control-ESC-Market-Growth-Projection-to-2021/159246

## Slide 31: Classic Hierarchical Approach
Decompose motion planning and control into stages
Route Planning
Merge Left
Yield to
Ped.
Park
Follow
Lane
Exit
Ramp
Merge
Right
Overtake
Behavior Planning
Path Planning
Sequence of roads and intersections
Target State Configurations
Detailed Path to Follow
Road Networks Traffic Information
Obstacles …
Model of the world around the car including predicted future states.
Model of the vehicle’s dynamics.
Local Control
Steering Angle
Acceleration
Notes: Path planning image courtesy of http://www.smart2zero.com/news/elektrobit-rolls-four-more-software-modules-autonomous-driving
Control image courtesy of https://www.egypt-business.com/Ticker/details/1738-Worldwide-Electronic-Stability-Control-ESC-Market-Growth-Projection-to-2021/159246

## Slide 32: Local Control
Basis for established technologies like electronic stability control
Use classic closed-loop controllers to actuate steering and acceleration along the planned path
Requires frequent control responses (real-time system) to correct for errors.
Common techniques often adopt locally linear approximations to the system
PID Controllers: Proportional-–integral—derivative controller corrects the steering and acceleration proportional to their deviation with damping
Linear Quadratic Regulators: Optimally controls a linear approximation of the system.
Local Control
Steering Angle
Acceleration

## Slide 33: Classic Hierarchical Approach
Decompose motion planning and control into stages
Local Control
Detailed Path to Follow
Model of the world around the car including predicted future states.
Model of the vehicle’s dynamics.
Route Planning
Merge Left
Yield to
Ped.
Park
Follow
Lane
Exit
Ramp
Merge
Right
Overtake
Behavior Planning
Path Planning
Sequence of roads and intersections
Target State Configurations
Road Networks Traffic Information
Obstacles …
More details can be found here in “A Survey of Motion Planning and Control Techniques for Self-driving Urban Vehicles”
Notes: Path planning image courtesy of http://www.smart2zero.com/news/elektrobit-rolls-four-more-software-modules-autonomous-driving
Control image courtesy of https://www.egypt-business.com/Ticker/details/1738-Worldwide-Electronic-Stability-Control-ESC-Market-Growth-Projection-to-2021/159246

## Slide 34: Classic Hierarchical Approach
Decompose motion planning and control into stages
Local Control
Detailed Path to Follow
Model of the world around the car including predicted future states.
Model of the vehicle’s dynamics.
Route Planning
Merge Left
Yield to
Ped.
Park
Follow
Lane
Exit
Ramp
Merge
Right
Overtake
Behavior Planning
Path Planning
Sequence of roads and intersections
Target State Configurations
Road Networks Traffic Information
Obstacles …
More details can be found here in “A Survey of Motion Planning and Control Techniques for Self-driving Urban Vehicles”
Where is the machine learning?
How are we using data?
Notes: Path planning image courtesy of http://www.smart2zero.com/news/elektrobit-rolls-four-more-software-modules-autonomous-driving
Control image courtesy of https://www.egypt-business.com/Ticker/details/1738-Worldwide-Electronic-Stability-Control-ESC-Market-Growth-Projection-to-2021/159246

## Slide 35: End-to-End Control (Behavior Cloning)
Advantages:
  Leverage large quantities of driving data without annotation
  Address complex scenarios without hand coded heuristics
Disadvantages:
  Requires substantial data in good and bad scenarios
  Doesn’t leverage domain knowledge
Cameras
LiDAR
Radar
IMU
GPS
Sensing
Steering
Accel & Breaking
Deep Learning
Imitation Learning
& Reinforcement Learning

## Slide 36: ALVINN 1989
Autonomous Land Vehicle in a Neural Network
Trained in simulation could follow some roads.

## Slide 37: Nvidia DAVE-2 System (2016)
Trained a deep neural network to control steering by behavior cloning (supervised loss).
Notes: https://www.youtube.com/watch?v=qhUvQiKec2U

## Slide 38: Limitations of End-to-End Approach
Doesn’t leverage physical models of vehicle control
Forced to learn and reason about scenes from driving supervision
  Model must learn the concepts of people, vehicles, obstacles directly from driving behavior demonstrations
Often doesn’t perform well in new situations
  Earlier examples were focused on the simple task of staying in the lane
Hybrid Approach
Leverage output of perception as well as the classic planning and control hierarchy and instead learn to output paths as a function of the output of perception.
  Example: Waymo ChauffeurNet

## Slide 39: ChauffeurNet
ChauffeurNet: Learning to Drive by Imitating the Best and Synthesizing the Worst
Rasterized Encoding of Current and Predicted States
Produced by Perception Pipelines
Predict future states of the world
Convolutional

## Slide 40: ChauffeurNet Examples